## Slide 1: Oakland Alameda Access Project
Providing Access and Connections

## Slide 2: Project Purpose and Need
Improve multimodal safety and reduce conflicts between regional and local traffic
Enhance bicycle and pedestrian accessibility and connectivity within the project study area
Improve mobility and accessibility for travelers between I-880, SR-260, City of Oakland downtown neighborhoods, and the City of Alameda
Reduce freeway-bound regional traffic and congestion on local roadways and in area neighborhoods

## Slide 3: Major Roadway Improvements
3
Construct right-turn from Posey Tube onto Horseshoe to NB Jackson St on-ramp
2
1
Realign WB I-980 Jackson St off-ramp and reconstruct 5th St
3
Widen NB I-880 Oak off-ramp, remove NB I-880 Broadway off-ramp, reconstruct 6th St for multi-modal access (Oak St to Washington St)
8
Reconfigure intersections at Broadway and 6th and 5th St
Restripe 7th St and improve intersections
4
Restripe Madison for 2-way travel between 4th to 6th St
5
Restripe Oak St for multimodal access (2-way cycle track from 3rd to 9th St)
7
Restripe Jackson for 1-way between 5th to 6th
6
8
8
CHINATOWN
Salvation Army
Oakland
Police
Chinese
Garden
Park
7
428
Alice
8 Orchid
JACK LONDON DISTRICT
2-way cycle track continuous to 9th St
2-way cycle track continuous to 3rd St
SOUTH
NORTH
1
2
3
4
5
6
Notes: A major overhaul of the roadway infrastructure is necessary to achieve the project purpose.
In particular, improvement #2 by creating a more direct access from vehicles leaving the Posey tube and bound for 880 North and improvement #3 which includes the removal of the I-880 Broadway off ramp, significant opportunities are available to drastically improve pedestrian safety on the local streets.

## Slide 4: Project Design – Selected Areas
6TH STREET LOOKING WEST TOWARD JACKSON STREET
Removal of the northbound I-880 Broadway off-ramp
CORNER OF 5TH STREET AND JACKSON STREET LOOKING WEST
Relocation of westbound I-980 Jackson Street off-ramp to the west along 5th Street
Removal of the northbound I-880 off-ramp
Horseshoe connector under I-880
Class IV Cycle Track
Reconstruction of east wall to construct right-turn from Posey Tube onto northbound I-880 Jackson Street on-ramp
Extension of 6th Street

## Slide 5: Types of Bicycle Facility
0.5 mile
0.4 mile
0.8 mile
0.2 mile
This project will add over 1.9 miles of new bike facilities and 0.7 miles of new sidewalks in Oakland!
Class I
Shared-Use Path
Class II
Bike Lane (incl. protected lane)
Class III
Bike Lane (incl. sharrow, Bike Blvd.)
Class IV
Cycle Track
Notes: The project adds over 3 miles of bicycle and pedestrian improvements including all four classes of bicycle facilities.

## Slide 6: Bike/Ped Safety and Access Improvements in Oakland
2
Family Bridges Lake Merritt Child Care
Chinese Garden Park
4
CHINATOWN
4
1
Chinese Garden Park
5
5
5
5
428
Alice
Fourth Street East
8 Orchid
5
5
2
1
3
1
Class I – 0.5 miles
Class II – 0.4 miles
Class III – 0.2 miles
Class IV – 0.8 miles
New sidewalk – 0.7 miles
3
4
2
5
Existing bike facility
Existing sidewalk
JACK LONDON DISTRICT
3
Notes: The City of Oakland, Chinatown, Jack London and Bike East Bay have been essential in the formulation of this preliminary Bike/Ped Safety and Access plan in Oakland. In the coming months, the details will continue to be refined.

## Slide 7: Project Area
2
Family Bridges Lake Merritt Child Care
Chinese Garden Park
4
CHINATOWN
4
1
Chinese Garden Park
5
5
5
5
428
Alice
Fourth Street East
8 Orchid
6
5
5
7
1
3

## Slide 8: Bike/Ped Safety and Access Improvements in Alameda
2
3
Widen and open walkway through Webster Tube and along Webster Street connecting to Mariner Square Loop (0.8 miles)
4
5
1
New Class II bike lane on Mariner Square Loop (0.3 miles)
Add crosswalks to connect ped/bike paths
New Class I path: Realign and widen path to 8 feet (0.3 miles)
Sidewalk extension on Mariner Square Loop and Mariner Square Drive (0.3 miles)
Target
Alameda
Landing
3
4
3
1
3
5
2
5
Notes: On the Alameda side of the tunnel, 0.5 mile of bicycle and pedestrian improvements provide safety, access and connectivity from the nearby facilities.
We thank Alameda City staff for their input in this preliminary plan.
The yellow highlights the improvements with or without Webster Tube improvements.
On Oakland side, Harrison St connects to Posey Tube.
On Alameda side, Posey Tube connects to Webster St. Webster Tube connects to Webster St Tube.

## Slide 9: Tube Improvements
3’
Notes: Improvements to the tunnel include the widening of an existing maintenance path to accommodate bicyclists. This improvement will serve as a two-fold allowing for access during the construction work at the Posey Oakland portal which is expected to be closed for an overall total of 18 months. After construction, the Webster path will remain and the current two way bicycle traffic going through the Posey tube will be separated into one-direction traffic. Bicyclists will go into Oakland via the Posey and into Alameda via the Webster.
Cost of Webster Tube and associated improvements is $7,400,000.
Posey Tube: Existing condition, there is one usable path through Posey Tube shared by bicyclist and pedestrians (3’ min) located on the right side of travel way. There is an existing maintenance path along the left side of travel way that is closed off and not accessible to the public. There is a utility line and call boxes along this path and there access from the Alameda side is not straight forward. The cost of relocating the fire protection line that sits in the way of path is expensive.
Webster Tube: Existing maintenance path is about 2.5’ wide and is currently not accessible to public. There is no existing path on the other side of Webster Tube.

## Slide 10: Aesthetics-Key Map
Incorporating Standards for Treatment of Historic Properties including Posey Tube
Adhering to Built Environment Treatment Plan
Compliance with Section 106 of the National Historic Preservation Act

## Slide 11: Aesthetics-Concept A (north of I-880)

## Slide 12: Aesthetics-Concept B (south of I-880)

## Slide 13: Construction Schedule
 | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 2028 |  |  | 
 | Winter | Spring | Summer | Fall | Winter | Spring | Summer | Fall | Winter | Spring | Summer | Fall | Winter | Spring | Summer | Fall
Stage 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Stage 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 14: Construction – Stage 1
Duration (1.5 YEARS)

## Slide 15: Construction – Stage 2
Duration (1 YEAR)

## Slide 16: I-980 Jackson Street Off Ramp Detour
Approximately 1 year to Demolish existing structure, realign and construct new structure
Detour will re-route drivers via 11th Street to Jackson Street

## Slide 17: Oak Street Off-Ramp Detour
Nighttime and Weekend closures for ramp improvements
Detour will re-route drivers via Broadway Exit and loop back on 7th Street

## Slide 18: SB I-880 On-Ramp Detour
Approximately 6 months to demolish and reconstruct retaining wall along SB I-880
Detour will re-route drivers via 7th Street to Madison Street to 5th Street

## Slide 19: Posey Tube Detour
Nighttime and Weekend closures for structure demolition and traffic control set up
Detour will re-route drivers via Lincoln Ave to Park Street to NB I-880 and exiting on Oak Street

## Slide 20: Webster Tube Detour
Nighttime closures for traffic control set up
Detour will re-route drivers via SB I-880 to 23rd Street to Park Street to Lincoln Ave

## Slide 21: Maintaining Pedestrian and Bike Mobility
Temporary Pedestrian Paths during construction will provide protected walkways around the construction work zones
When existing Class I, II and IV bike facilities are impacted by construction activities Class III bike routes will be provided

## Slide 22: Project Schedule
Project Milestone | Schedule By Phase
Scoping | Summer 2009 - Spring 2011
Preliminary Engineering/Environmental | Fall 2017 to Early 2022
Final Design | February 2022 to Fall 2024
Project Advertisement/Bidding Process | Early 2022 to Fall 2024
Construction | Spring 2025 to Summer 2028
*Design has achieved 95% milestone and is progressing to 100% | 

## Slide 23: Questions

## Slide 24: Thank you!